MATERIAL SAFETY DATA SHEET

CHEMAT TECHNOLOGY INC.

# 9036 Winnetka Avenue

Northridge, CA 91324

Ph# 818) 727-9786/Fax# (818)727-9477

-----------------------------------------------IDENTIFICATION-----------------------------------------------

CHEMICAL NAME: Aluminum isopropoxide, 99.99%, 5g/100ml in isopropanol

CATALOG NUMBER: A1022	PURITY: 99.99% (metal basis)

FORMULA: Al(OC3H7i)3 	FORMULA WEIGHT: 204.25

TSCA: Not listed

CHEMICAL FAMILY: Metal alkoxides

-------------------------------------HAZARDOUS INGREDIENTS---------------------------------------

HAZARDOUS INGREDIENTS:	%

Title compound		   5	ACGIH/TLV: No data

OSHA/PEL: No data

Isopropanol                             	 95	ACGIH/TLV: 400ppm

OSHA/PEL:  400ppm

------------------------------------------------PHYSICAL DATA-----------------------------------------------

APPEARANCE AND ODOR: Clear solution

BOILING POINT:  82oC (Isopropanol)

FREEZING/MELTING POINT:  -90oC (Isopropanol)

SOLUBILITY IN WATER: Reacts with water, decomposes.

--------------------------------------------------FIRE HAZARD-------------------------------------------------

FLASH POINT:  55F (12.78oC) (Isopropanol)

AUTOIGNITION TEMPERATURE: 810F (432.22oC) (Isopropanol)

EXTINGUISHING MEDIA: For small fires, use dry chemical, carbon dioxide, water spray or alcohol-resistant foam.  Use water spray to cool fire-exposed containers.  Water may be ineffective.

SPECIAL FIRE FIGHTING PROCEDURES: No special fire fighting procedures needed, use normal procedures which include wearing NIOSH/MSHA approved self contained breathing apparatus, flame and chemical resistant clothing; hats, boots and gloes.  If without risk remove material from fire area.

-----------------------------------------------HEALTH HAZARD----------------------------------------------

MODE OF ENTRY:

INGESTION: May cause GI pain, cramps, nausea, vomiting and diarrhea.  Ingestion of isopropyl alcohol may cause drowsiness, unconsciousness and death.

SKIN CONTACT: Cause irritation or burns.  May cause allergic ski reactions.

EYE CONTACT: Irritant.  Causes irritation or burns.

INHALATION: May cause irritation.  Large concentrations may have narcotic effect.

MEDICAL CONDITIONS, IF ANY AGGRAVATED BY CHEMICAL:  No data.

OTHER HEALTH HAZARDS:  No data

MOST LIKELY ROUTES OF ENTRY:  Ingestion/inhalation

CHRONIC EFFECTS:  No data for ingestion, inhalation, eye contact.  For skin 	contact it may cause dermatitis.

EMERGENCY AND FIRST AID PROCEDURES:

INHALATION: No specific information available, one should obtain medical 	attention.

SKIN CONTACT: Remove contaminated clothing, flood skin with large amounts 	of water.  If irritation persists seek medical attention.

EYE CONTACT: Immediately flush eyes, including under eyelids, with large 	amounts of water for at least 15 minutes.  Call a physician.

INGESTION: No data available but one should obtain medical attention.

-----------------------------------------------REACTIVITY DATA--------------------------------------------

STABILITY: Stable.

CONDITIONS TO AVOID: Exposure to moisture, air.

INCOMPATIBILITY: Moisture, sparks, open flames, oxidizers, water, acids.

HAZARDOUS DECOMPOSITION PRODUCTS: Isopropanol, aluminum hydroxide, aluminum oxide, CO, CO2 .

HAZARDOUS POLYMERIZATION: None/will not occur.

---------------------------------ENVIRONMENTAL INFORMATION--------------------------------

SPILL OR LEAKAGE PROCEDURES: Wearing full protective clothing and respiratory protection, eliminate all sources of ignition.  Cover spill with dry sand or dry ground vermiculite, mix well and carefully transfer to a well marked container.  close container tightly.

WASTE DISPOSAL: Consult state, local, or federal EPA regulations for proper disposal.

----------------------------------PROTECTION AND PRECAUTIONS--------------------------------

VENTILATION REQUIREMENTS: Handle in a glove bag or box with dry, inert atmosphere.

RESPIRATORY PROTECTION: NIOSH/MSHA approved respirator with an organic vapor cartridge.

PROTECTIVE GLOVES: Rubber

EYE/FACE PROTECTION: ANSI approved safety goggles

HANDLING AND STORAGE: Handle and store the material under an inert atmosphere of nitrogen or argon.  Keep away from heat.

OTHER PRECAUTIONS: Keep container tightly closed.  Store in a cool, dry, well-ventilated area.  Wash thoroughly after use. Lab coat and apron, flame and chemical resistant coveralls, eyewash capable of sustained flushing, safety drench shower and hygienic facilities for washing.

---------------------------------------------------------------------------------------------------------------------------

The information herein is believed to be accurate and reliable as of the date compiled.  However, Chemat Technology, Inc. makes no representation, warranty or guarantee of any kind with respect to the information on this data sheet or any use of the product based upon this information.

DATE PREPARED:  September 2000