MATERIAL SAFETY DATA SHEET

CHEMAT TECHNOLOGY, INC.

9036 Winnetka Avenue

Northridge, CA 91324

(818) 727-9786, (818) 727-9477 FAX

-----------------------------------------------IDENTIFICATION-----------------------------------------------

CHEMICAL NAME: Barium 2-ethylhexanoate in hexane, 10g/100ml

CATALOG NUMBER: B124

FORMULA: Ba(OOCC7H15)2	                FORMULA WEIGHT: 423.68

TSCA:  listed in the TSCA inventory

-------------------------------------HAZARDOUS INGREDIENTS---------------------------------------

HAZARDOUS INGREDIENTS:	%

Title compound                                  10	ACGIH(TLV): No data

OSHA/PEL: No data

Hexane                                                90            ACGIH TWA: 500ppm

OSHA TWA: 500ppm

ACGIH STEL: 1000ppm

OSHA STEL: 1000ppm

------------------------------------------------PHYSICAL DATA-----------------------------------------------

APPEARANCE : brown liquid.

MELTING POINT: -95(C(hexane)	BOILING POINT: 65(C(hexane)

VAPOR PRESSURE: 150 mmHg @68F(hexane)	SPECIFIC GRAVITY: 0.68(hexane)

SOLUBILITY IN WATER: insoluble

--------------------------------------------------FIRE HAZARD-------------------------------------------------

FLASH POINT: 0 F(-18(C) (hexane)

AUTOIGNITION TEMPERATURE: No data

EXTINGUISHING MEDIA: Use carbon dioxide or dry powder as extinguishing agents.

SPECIAL FIRE FIGHTING PROCEDURES: Burning material may release toxic and corrosive fumes. Leave the area unless fitted with a self-contained breathing apparatus and fire protective clothing.

UNUSUAL FIRE OR EXPLOSION HAZARDS:  No unusual fire or explosion hazards.

-----------------------------------------------HEALTH HAZARD----------------------------------------------

MODE OF ENTRY:

INHALATION: No

SKIN CONTACT: No

EYE CONTACT: No

INGESTION: Yes

CARCINOGENCITY:

NTP: Not known

IARC: Not known

OSHA: Not known

EMERGENCY AND FIRST AID PROCEDURES:

INHALATION: Remove the victim to fresh air and seek medical attention if coughing, shortness of breath or irritation persists.

SKIN CONTACT: Wash the affected area with soap and water for at least 5 minutes.

EYE CONTACT: Immediately flush eyes, including under eyelids, with large amounts of water for at least 15 minutes.  Call a physician.

INGESTION: Give the victim plenty of water and seek immediate medical attention.

-----------------------------------------------REACTIVITY DATA--------------------------------------------

STABILITY: Air and moisture stable.

CONDITIONS TO AVOID: Contact with ignition source or heat.

INCOMPATIBILITY: Oxidizing agents.

HAZARDOUS DECOMPOSITION PRODUCTS: CO, CO2, Barium oxide, and organic fumes

HAZARDOUS POLYMERIZATION: None

---------------------------------ENVIRONMENTAL INFORMATION--------------------------------

SPILL OR LEAKAGE PROCEDURES: Wearing full protective equipment, eliminate all sources of ignition.  Cover spill with dry sand or vermiculite.  Sweep up the mixture and dispose of properly.

WASTE DISPOSAL: Consult state, local, or federal EPA regulations for proper disposal.

----------------------------------PROTECTION AND PRECAUTIONS--------------------------------

VENTILATION REQUIREMENTS: Hood.

RESPIRATORY PROTECTION: NIOSH/MSHA approved respirator with an organic vapor cartridge.

PROTECTIVE GLOVES: Rubber

EYE/FACE PROTECTION: ANSI approved safety goggles

HANDLING AND STORAGE: Store the material in a sealed containers.  Keep away from heat and moisture.

OTHER PRECAUTIONS: No special precautions necessary. To minimize exposure handle the material in an efficient fume hood.

---------------------------------------------------------------------------------------------------------------------------

The information herein is believed to be accurate and reliable as of the date compiled.  However, Chemat Technology, Inc. makes no representation, warranty or guarantee of any kind with respect to the information on this data sheet or any use of the product based upon this information.

DATE PREPARED:  May 1, 2000