MATERIAL SAFETY DATA SHEET

CHEMAT TECHNOLOGY INC.

9036 Winnetka Avenue

Northridge, CA 91324

(818) 727-9786, (818) 727-9477 FAX

-----------------------------------------------IDENTIFICATION-------------------------------------

CHEMICAL NAME: Gadolinium 2-methoxyethoxide, 5g/100ml in 2-methoxyethanol

CATALOG NUMBER: G108	PURITY: 99% (metal based)

FORMULA: Gd(OCH2CH2OCH3)3	FORMULA WEIGHT: 382.35

TSCA: listed on TSCA inventory

CHEMICAL FAMILY: Metal alkoxide

-------------------------------------HAZARDOUS INGREDIENTS-------------------------------

## HAZARDOUS INGREDIENTS:	                     %

Gd(OCH2CH2OCH3)3	                      5	ACGIH(TLV): No data

OSHA/PEL: No data

2-methoxyethanol, CAS#: 109-86-4                      95                     TLV-TWA: 25ppm /skin			                                                                TLV-STEL: 35ppm /skin

------------------------------------------------PHYSICAL DATA--------------------------------------

APPEARANCE AND ODOR: yellowish clear solution.

MELTING POINT: -85oC (2-methoxyethanol)

BOILING POINT: 124oC to 125oC (2-methoxyethanol)

VAPOR PRESSURE: 6.2mm@ 20oC (2-methoxyethanol)

SPECIFIC GRAVITY: 0.965(2-methoxyethanol)

VAPOR DENSITY: 2.62G/L(2-methoxyethanol)

SOLUBILITY IN WATER: Reacts with moisture

--------------------------------------------------FIRE HAZARD----------------------------------------

FLASH POINT: 115 F (2-methoxyethanol)

EXPLOSION LIMITS: (2-methoxyethanol)

upper: 24.5% 		lower: 2.5%

EXTINGUISHING MEDIA: Carbon dioxide, dry chemical powder or appropriate foam.  Water may be effective for cooling, but may not effect extinguishment.

SPECIAL FIRE FIGHTING PROCEDURES: Wear self-contained breathing apparatus and protective clothing to prevent contact with skin and eyes.  Use water spray to cool fire-exposed containers.

UNUSUAL FIRE AND EXPLOSION HAZARDS: Conbustible liquid. Forms explosive mixtures in air.

-----------------------------------------------HEALTH HAZARD-------------------------------------

EFFECTS OF OVEREXPOSURE:

ACUTE EFFECTS:

Readily abaorbed through skin.

Harmful if swallowed, inhaled, or absorbed through skin.

Causes severe irritation.

High concentrations are extremely destructive to tissues of the mucous membranes and upper 	respiratory tract, eyes and skin.

Symptoms of exposure may include burning sensation, coughing, wheezing, laryngitis, shortness of breath, headache, nausea and vomiting.

Exposure can cause:

Lung irritation, chest pain and edema which may be fatal.

CHRONIC EFFECTS:

May cause nervous system disturbances. Methoxyethanol may cause harm to the unborn baby. The target organs are blood, kidneys, liver, lungsmale reproductive system, immune system, thymus, and bornn marrow.

-----------------------------------------------REACTIVITY DATA-----------------------------------

STABILITY: Moisture-sensitive material.

CONDITIONS TO AVOID: Contact with ignition source or heat.

HAZARDOUS DECOMPOSITION PRODUCTS: CO, CO2, gadolinium oxide and organic fumes

HAZARDOUS POLYMERIZATION: None

---------------------------------ENVIRONMENTAL INFORMATION-------------------------

SPILL OR LEAKAGE PROCEDURES: Wearing full protective equipment, eliminate all sources of ignition.  Cover spill with dry sand or vermiculite.  Sweep up the mixture and dispose of properly.

WASTE DISPOSAL: Consult state, local, or federal EPA regulations for proper disposal.

----------------------------------PROTECTION AND PRECAUTIONS------------------------

VENTILATION REQUIREMENTS: Glove bag or box with dry, inert atmosphere.

RESPIRATORY PROTECTION: NIOSH/MSHA approved respirator with an organic vapor cartridge.

PROTECTIVE GLOVES: Rubber

EYE/FACE PROTECTION: ANSI approved safety goggles

HANDLING AND STORAGE: Handle and store the material under an inert atmosphere of nitrogen or argon.  Keep away from heat.

OTHER PRECAUTIONS: The material will react with moisture.  Lab coat and apron, flame and chemical resistant coveralls, eyewash capable of sustained flushing, safety drench shower and hygienic facilities for washing.

----------------------------------------------------------------------------------------------------------------

The information herein is believed to be accurate and reliable as of the date compiled.  However, Chemat Technology Inc. makes no representation, warranty or guarantee of any kind with respect to the information on this data sheet or any use of the product based upon this information.

DATE PREPARED: February 13, 2003