MATERIAL SAFETY DATA SHEET

CHEMAT TECHNOLOGY, INC.

9036 Winnetka Avenue

Northridge, CA 91324

(818) 727-9786, (818) 727-9477 FAX

-----------------------------------------------IDENTIFICATION-------------------------------------

CHEMICAL NAME: Germanium (IV) ethoxide

CATALOG NUMBER: G302

FORMULA: Ge(OC2H5)4	FORMULA WEIGHT: 252.84

CHEMICAL FAMILY: Metal alkoxide

CAS #:  14165-55-0

-------------------------------------HAZARDOUS INGREDIENTS-------------------------------HAZARDOUS INGREDIENTS:	%

Title compound	100	ACGIH(TLV): No data

OSHA/PEL: No data

------------------------------------------------PHYSICAL DATA--------------------------------------

APPEARANCE, ODOR: Clear colorless liquid

MELTING POINT:  -81oC

BOILING POINT:  168oC; 55oC/0.2mm

SOLUBILITY IN WATER:  Hydrolyzes slowly

SOLUBILITY IN ORGANICS:  Readily soluble in hydrocarbons

--------------------------------------------------FIRE HAZARD----------------------------------------

FLASH POINT: 62oC

AUTOIGNITION TEMPERATURE: No data

EXPOSURE LIMITS:  TLV 8hr TWA:  0.2ppm or 0.6mg/m3 GeO2

TLV STEL:  0.6 or 1.8mg/m3 GeO2

FIRE AND EXPLOSION HAZARD:  Flammable.

EXTINGUISHING MEDIA:  Use alcohol resistant foam or dry chemical powder.  Water spray (not jet) may be used.  For small fires, carbon dioxide is also suitable.

-----------------------------------------------HEALTH HAZARD-------------------------------------MODE OF ENTRY:

INHALATION: Yes

SKIN CONTACT: Yes

EYE CONTACT: Yes

INGESTION: Yes

CARCINOGENCITY:

NTP: Not known

IARC: Not known

OSHA: Not known

EFFECTS OF OVEREXPOSURE:

Germanium and its compounds are only slightly toxic, acute LD50 100-1000mg/kg.  The dehydrating nature of germanium ethoxide is probably more significant causing irritation and burns if not removed.

INHALATION:  Harmful by inhalation.

SKIN:  May cause irritation to skin.  Should avoid contact with the skin.

EYES:  Assumed to be harmful to the eyes.

INGESTION:  Harmful if swallowed.

EMERGENCY AND FIRST AID PROCEDURES:

INHALATION: Remove the victim to fresh air and seek medical attention if coughing, shortness of breath or irritation persists.

SKIN CONTACT: Wash the affected area with ethanol first, then soap and water for at least 5 minutes.

EYE CONTACT: Immediately flush eyes, including under eyelids, with large amounts of water for at least 15 minutes.  Call a physician.

INGESTION: Give the victim plenty of water and seek immediate medical attention.

-----------------------------------------------REACTIVITY DATA-----------------------------------

STABILITY:  Decomposes slowly on contact with water.

CONDITIONS TO AVOID: Contact with moisture, ignition source or heat.

INCOMPATIBILITY:  Water, Oxidizing agents.

HAZARDOUS DECOMPOSITION PRODUCTS: Carbon monoxide, carbon dioxide, germanium oxide and toxic organic fumes.

HAZARDOUS POLYMERIZATION: None

---------------------------------ENVIRONMENTAL INFORMATION-------------------------

SPILL OR LEAKAGE PROCEDURES:  Extinguish all sources of ignition.  Isolate area.  Shut off leak.  Avoid breathing vapors.  Contain spill with dry absorbent.  Collect up and transfer mixed with dry sand to containers.  Wash spill site with water.

WASTE DISPOSAL: Consult state, local, or federal EPA regulations for proper disposal.

STORAGE AND HANDLING:  Ensure no sources of ignition.  Handle under inert gas.  Avoid inhaling vapor, or contact with eyes, skin or clothing.  Adequate ventilation must be provided.  Store in secure containers away from water and sources of ignition.

----------------------------------PROTECTION AND PRECAUTIONS------------------------

VENTILATION REQUIREMENTS: Local exhaust is recommended.  Mechanical is recommended.

RESPIRATORY PROTECTION: NIOSH/MSHA approved respirator with an organic vapor cartridge.

PROTECTIVE GLOVES: Rubber

EYE/FACE PROTECTION: ANSI approved safety goggles.

HANDLING AND STORAGE: Stored in sealed containers.

OTHER PRECAUTIONS:  Lab coat and apron, flame and chemical resistant coveralls, eyewash capable of sustained flushing, safety drench shower and hygienic facilities for washing.

----------------------------------------------------------------------------------------------------------------

The information herein is believed to be accurate and reliable as of the date compiled.  However, Chemat Technology Inc. makes no representation, warranty or guarantee of any kind with respect to the information on this data sheet or any use of the product based upon this information.

DATE PREPARED: October 31, 2005