MATERIAL SAFETY DATA SHEET

CHEMAT TECHNOLOGY, INC.

9036 Winnetka Avenue

Northridge, CA 91324

(818) 727-9786, (818) 727-9477 FAX

-----------------------------------------------IDENTIFICATION-----------------------------------------------

CHEMICAL NAME: Indium (III) methoxyethoxide, in methoxyethanol

CATALOG NUMBER: I103

FORMULA: In(OC2H4OCH3)3 in HOC2H4OCH3	FORMULA WEIGHT: 340.08

TSCA: not listed in the TSCA inventory 	 methoxyethanol: listed

CHEMICAL FAMILY: Metal alkoxide solution

-------------------------------------HAZARDOUS INGREDIENTS---------------------------------------

HAZARDOUS INGREDIENTS:	%

Title compound	16	ACGIH(TLV): No data

OSHA/PEL: No data

Methoxyethanol	84	ACGIH(TLV): 25 ppm

OSHA/PEL: 25 ppm

------------------------------------------------PHYSICAL DATA-----------------------------------------------

APPEARANCE AND ODOR: Light yellow solution

MELTING POINT: No data 	BOILING POINT: 124.5oC (2-methoxyethanol)

VAPOR PRESSURE: No data 	SPECIFIC GRAVITY: No data

SOLUBILITY IN WATER: Hydrolyzes in water

--------------------------------------------------FIRE HAZARD-------------------------------------------------

FLASH POINT: 115oF (2-methoxyethanol)

AUTOIGNITION TEMPERATURE: 545oF (2-methoxyethanol)

EXTINGUISHING MEDIA: Alcohol foam, carbon dioxide or dry chemical.

SPECIAL FIRE FIGHTING PROCEDURES: Flammable liquid.  Burning material may release toxic and corrosive fumes.  Use normal fire fighting procedures which include wearing NIOSH/MSHA approved self-contained breathing apparatus, flame, and chemical resistant clothing; hats, boots, and gloves.  Leave the area unless fitted with a self-contained breathing apparatus and fire protective clothing.

UNUSUAL FIRE OR EXPLOSION HAZARDS: Flammable liquid.  Dangerous when exposed to heat or flame.  Can react with oxidizing materials.  Violent reaction with H2O2.

-----------------------------------------------HEALTH HAZARD----------------------------------------------

MODE OF ENTRY: 			CARCINOGENCITY:

INHALATION: Yes				NTP: Not known

SKIN CONTACT: Yes 			IARC: Not known

EYE CONTACT: Yes			OSHA: Not known

INGESTION: Yes

EFFECTS OF OVEREXPOSURE:

Indium compounds: Indium compounds injected into experimental animals are found to be highly toxic.  Effects include reduced food and water consumption with accompanying weight loss, pulmonary edema, necrotizing pneumonia, blood damage, liver and kidney damage, hind leg paralysis in rabbits and damage to the brain, heart, adrenals and spleen.

2-Methoxyethanol: inhalation TCLO (human) = 25ppm leads to central nervous system effects.  May cause reversible or irreversible changes to exposed tissue, not permanent injury or death and can cause considerable discomfort via oral, intravenous, and inhalation routes.  When used under conditions which do not require the application of heat, this material probably presents little hazard to health.  Reflexes may be exaggerated or abnormal in character, and may be accompanied by complaints of drowsiness and fatigue.  Tremors may be present.  Severe damage probably takes the form of aplastic anemia.

EMERGENCY AND FIRST AID PROCEDURES:

INHALATION: Remove the victim to fresh air and seek medical attention if coughing, shortness of breath or irritation persists.

SKIN CONTACT: Wash the affected area with soap and water for at least 5 minutes.

EYE CONTACT: Immediately flush eyes, including under eyelids, with large amounts of water for at least 15 minutes.  Call a physician.

INGESTION: Give the victim plenty of water and seek immediate medical attention.

-----------------------------------------------REACTIVITY DATA--------------------------------------------

STABILITY: Moisture-sensitive material.

CONDITIONS TO AVOID: Heat, ignition source, reaction with H2O2, and prolonged contact with air.

INCOMPATIBILITY: Moisture, oxidizing materials, heat, H2O2.

HAZARDOUS DECOMPOSITION PRODUCTS: CO, CO2, indium oxide, and organic fumes.

HAZARDOUS POLYMERIZATION: None

---------------------------------ENVIRONMENTAL INFORMATION--------------------------------

SPILL OR LEAKAGE PROCEDURES: The material will evaporate at room temperature.  Leave the area unless fitted with a self-contained breathing apparatus, or until the vapors have dispersed.  Larger spills can be absorbed into vermiculite or other suitable chemical adsorbent.  Sweep up the material and dispose of properly.

WASTE DISPOSAL: Consult state, local, or federal EPA regulations for proper disposal.

----------------------------------PROTECTION AND PRECAUTIONS--------------------------------

VENTILATION REQUIREMENTS: Local exhaust

RESPIRATORY PROTECTION: NIOSH/MSHA approved respirator with an organic vapor cartridge.

PROTECTIVE GLOVES: Rubber

EYE/FACE PROTECTION: ANSI approved safety goggles

HANDLING AND STORAGE: Handle and store the material under an inert atmosphere of nitrogen or argon.  Keep away from heat.

OTHER PRECAUTIONS: The material will react with moisture.  Lab coat and apron, flame and chemical resistant coveralls, eyewash capable of sustained flushing, safety drench shower and hygienic facilities for washing.

---------------------------------------------------------------------------------------------------------------------------

The information herein is believed to be accurate and reliable as of the date compiled.  However, Chemat Technology, Inc. makes no representation, warranty or guarantee of any kind with respect to the information on this data sheet or any use of the product based upon this information.

DATE PREPARED: Sep. 2011