MATERIAL SAFETY DATA SHEET

CHEMAT TECHNOLOGY INC.

9036 Winnetka Avenue

Northridge, CA 91324

(818) 727-9786, (818) 727-9477 FAX

-----------------------------------------------IDENTIFICATION-------------------------------------

CHEMICAL NAME: Lanthanum 2-ethylhexanoate, 10g/100ml in hexane

CATALOG NUMBER: L122

FORMULA: La(OOCC7H15)3	FORMULA WEIGHT: 568.18

CHEMICAL FAMILY: Metal carboxilate

-------------------------------------HAZARDOUS INGREDIENTS-------------------------------HAZARDOUS INGREDIENTS:	%

Title compound	10	ACGIH(TLV): No data

OSHA/PEL: No data

Hexane                                                90	ACGIH(TLV): 50ppm

OSHA/PEL: 50ppm

------------------------------------------------PHYSICAL DATA--------------------------------------

APPEARANCE, ODOR: Brown solution, faint odor (hexane)

MELTING POINT: -139F (-95oC) (hexane)

BOILING POINT, INITIAL:  136F (58oC) (hexane)

VAPOR PRESSURE: 124 mmHg @20oC (hexane)	SPECIFIC GRAVITY:  0.7 (hexane)

VAPOR DENSITY: 3.0 (hexane)

SOLUBILITY IN WATER:  Hydrolyzes in water.

--------------------------------------------------FIRE HAZARD----------------------------------------

FLASH POINT: -7F (-22oC) (hexane)

AUTOIGNITION TEMPERATURE: 437F (223oC) (hexane)

FLAMMABILITY CLASS (OSHA):  1B (hexane)         LEL:  1.1%		UEL:  7.5%

FIRE AND EXPLOSION HAZARD:  Dangerous fire hazard when exposed to heat or flame.  Vapors are heavier than air and may travel a considerable distance to a source of ignition and flash back.  Vapor-air mixtures are explosive above flash point.  Due to low electroconductivity of the substance, flow or agitation may generate electrostatic charges resulting in sparks with possible ignition.

EXTINGUISHING MEDIA:  Dry chemical, carbon dioxide, water spray or regular foam.  For larger fires, use water spray, fog or regular foam.

UNUSUAL FIRE OR EXPLOSION HAZARDS:  Move containers from fire area if you can do it without risk.  Apply cooling water to sides of containers that are exposed to flames until well after fire is out.  Extinguish only if flow can be stopped; use water in flooding amounts as fog.  Solid streams may not be effective.  Cool containers with flooding quantities of water.  Apply from as far a distance as possible.  Avoid breathing toxic vapors; keep upwind.  Water may be ineffective.

-----------------------------------------------HEALTH HAZARD-------------------------------------MODE OF ENTRY:

INHALATION: Yes

SKIN CONTACT: Yes

EYE CONTACT: Yes

INGESTION: Yes

CARCINOGENCITY:

NTP: Not known

IARC: Not known

OSHA: Not known

EFFECTS OF OVEREXPOSURE:

Lanthanum and other lanthanons can cause delayed blood clotting, leading to hemorrhages.  Has caused liver injury in exper animals.

INGESTION:  May cause central nervous system effects, headache, nausea, vomitting, vertigo, bronchial and general intestinal irritation with abdominal swelling and pain.  May vaporize when aspirated into the tracheobronchial tree with a resultant rapid dilution of alveolar air and marked fall in its oxygen content, with consequent brain damage or cardiac arrest.

SKIN CONTACT:  Vapor may cause irritation with redness.  Repeated or prolonged contact may cause dermatitis due to defatting.  Blister formation, itching, erythema, pigmentation and pain have been reported.  Skin exposures may enhance neurotoxic effects from inhalation exposure.

EYE CONTACT:  Contact may cause irritation with redness and pain.  Vapors at 880ppm for 15 minutes caused irritation.

INHALATION:  Can cause respiratory tract irritation. May produce headache, nausea, and dizziness.  Prolonged exposure may cause effects as in acute exposure as well as in memory loss, aching muscles, sensory loss in feet and hands, blurred vision.

EMERGENCY AND FIRST AID PROCEDURES:

INHALATION: Remove the victim to fresh air and seek medical attention if coughing, shortness of breath or irritation persists.

SKIN CONTACT: Wash the affected area with ethanol first, then soap and water for at least 5 minutes.

EYE CONTACT: Immediately flush eyes, including under eyelids, with large amounts of water for at least 15 minutes.  Call a physician.

INGESTION: Give the victim plenty of water and seek immediate medical attention.

-----------------------------------------------REACTIVITY DATA-----------------------------------

STABILITY:  Decomposes slowly in contact with moist air and rapidly in contact with water.

CONDITIONS TO AVOID: Contact with moisture, ignition source or heat.

INCOMPATIBILITY:  Water, Oxidizing agents.

HAZARDOUS DECOMPOSITION PRODUCTS:  Lanthanum oxide,  CO, CO2, organic fumes.

HAZARDOUS POLYMERIZATION: None

---------------------------------ENVIRONMENTAL INFORMATION-------------------------

SPILL OR LEAKAGE PROCEDURES: Wearing full protective equipment, eliminate all sources of ignition.  Cover spill with dry sand or vermiculite.  Sweep up the mixture and dispose of properly.

WASTE DISPOSAL: Consult state, local, or federal EPA regulations for proper disposal.

----------------------------------PROTECTION AND PRECAUTIONS------------------------

VENTILATION REQUIREMENTS: Local exhaust is recommended.  Mechanical is recommended.

RESPIRATORY PROTECTION: NIOSH/MSHA approved respirator with an organic vapor cartridge.

PROTECTIVE GLOVES: Rubber

EYE/FACE PROTECTION: ANSI approved safety goggles

HANDLING AND STORAGE: Stored in sealed containers.

OTHER PRECAUTIONS:  Lab coat and apron, flame and chemical resistant coveralls, eyewash capable of sustained flushing, safety drench shower and hygienic facilities for washing.

----------------------------------------------------------------------------------------------------------------

The information herein is believed to be accurate and reliable as of the date compiled.  However, Chemat Technology, Inc. makes no representation, warranty or guarantee of any kind with respect to the information on this data sheet or any use of the product based upon this information.

DATE PREPARED: August, 2009