MATERIAL SAFETY DATA SHEET

CHEMAT TECHNOLOGY, INC.

9036 Winnetka Avenue

Northridge, CA 91324

(818) 727-9786, (818) 727-9477 FAX

-----------------------------------------------IDENTIFICATION-----------------------------------------------

CHEMICAL NAME:  Lithium tantalum butoxide (in n-butanol)

CATALOG NUMBER: LT110-1 	PURITY: 99+%

FORMULA: LiTa(OC4H9)6 in H9C4OH	FORMULA WEIGHT: 625.89

TSCA: not listed in TSCA inventory

CHEMICAL FAMILY: Metal alkoxide solution

-------------------------------------HAZARDOUS INGREDIENTS---------------------------------------

HAZARDOUS INGREDIENTS:	%

Title compound	5	ACGIH(TLV): No data

OSHA/PEL: No data

Butanol	95	ACGIH(TLV): 50ppm

OSHA/PEL: 50ppm

------------------------------------------------PHYSICAL DATA-----------------------------------------------

APPEARANCE AND ODOR: yellowish liquid

MELTING POINT: No data 	BOILING POINT: 243F(n-butanol)

VAPOR PRESSURE: No data 	SPECIFIC GRAVITY: No data

SOLUBILITY IN WATER: Reacts with water

--------------------------------------------------FIRE HAZARD-------------------------------------------------

FLASH POINT: 84F

AUTOIGNITION TEMPERATURE: 650F

EXTINGUISHING MEDIA: Flammable liquid.  Use alcohol foam, carbon dioxide or dry chemical extinguishing agents.  Water may be used to keep fire exposed containers cool.

SPECIAL FIRE FIGHTING PROCEDURES: Flammable liquid. Material readily ignited with flame, sparks, friction or heat. Burning material may release toxic and corrosive fumes. Vapors can flow along surfaces to distant ignition sources and flash back.Use normal fire fighting procedures which include wearing NIOSH/MSHA approved self-contained breathing apparatus, flame, and chemical resistant clothing; hats, boots, and gloves.  Leave the area unless fitted with a self-contained breathing apparatus and fire protective clothing.

UNUSUAL FIRE OR EXPLOSION HAZARDS: Flammable liquid.  Vapors can form  explosive mixtures with air.

-----------------------------------------------HEALTH HAZARD----------------------------------------------

MODE OF ENTRY: 				CARCINOGENCITY:

INHALATION: Yes					NTP: Not known

SKIN CONTACT: Yes 				IARC: Not known

EYE CONTACT: Yes				OSHA: Not known

INGESTION: Yes

EFFECTS OF OVEREXPOSURE:

INHALATION: Lithium compounds have been implicated in development of aplastic anemia.  Lithium ion has central nervous system toxicity.  Some tantalum compounds have been suspected of causing mild fibrosis of the lungs. May cause irritation of the nose, throat, and lungs.  Exposure to high concentrations has a narcotic effect, producing symptoms of drowsiness, headache, staggering, unconciousness, and possibly death.

SKIN CONTACT: Lithium oxide, hydroxide, carbonate, etc., are strong bases and these solutions in water are very caustic. N-butanol can cause skin irritation, can be absorbed through the skin in harmful amounts. Prolonged and/or repeated contact may cause defatting of the skin and dermatitis.

EYE CONTACT:  Vapors may irritate eyes. Splashes may cause severe irritation, possible corneal burns and eye damage.

INGESTION: Large of doses of lithium compounds have caused dizziness and prostation.  Can cause kidney damage, anorexia, nausea, apathy, coma and death.  Aspiration of n-butanol can be hazardous.  It may cause liver damage. Aspiration of n-butanol into the lungs may cause chemical pneumonitis, which my be fatal.

CHRONIC:  Not available. Repeated eye exposure may cause visual abnormalities including blurred vision and photosensitivity.  Repeated exposure in combination with constant, loud noise can produce hearing loss and vertigo.

EMERGENCY AND FIRST AID PROCEDURES:

INHALATION: Remove the victim to fresh air and seek medical attention if coughing, shortness of breath or irritation persists.

SKIN CONTACT: Wash the affected area with soap and water for at least 5 minutes.

EYE CONTACT: Immediately flush eyes, including under eyelids, with large amounts of water for at least 15 minutes.  Call a physician.

INGESTION: Give the victim plenty of water and seek immediate medical attention.

-----------------------------------------------REACTIVITY DATA--------------------------------------------

STABILITY: Moisture-sensitive material.

CONDITIONS TO AVOID: Contact with ignition source or heat.

INCOMPATIBILITY: Moisture, heat, aluminum, chromium trioxide, strong oxidizers, organic peroxides.

HAZARDOUS DECOMPOSITION PRODUCTS: CO, CO2, butanol, lithium hydroxide, tantalum oxide, and organic fumes

HAZARDOUS POLYMERIZATION: None

---------------------------------ENVIRONMENTAL INFORMATION--------------------------------

SPILL OR LEAKAGE PROCEDURES: Wearing full protective equipment, eliminate all sources of ignition.  Cover spill with dry sand or vermiculite.  Sweep up the mixture and dispose of properly.

WASTE DISPOSAL: Consult state, local, or federal EPA regulations for proper disposal.

----------------------------------PROTECTION AND PRECAUTIONS--------------------------------

VENTILATION REQUIREMENTS: Glove bag or box with dry, inert atmosphere.

RESPIRATORY PROTECTION: NIOSH/MSHA approved respirator with an organic vapor cartridge.

PROTECTIVE GLOVES: Rubber

EYE/FACE PROTECTION: ANSI approved safety goggles

HANDLING AND STORAGE: Handle and store the material underan inert atmosphere of nitrogen or argon.  Keep away from heat.

OTHER PRECAUTIONS: The material will react with air and moisture.  Lab coat and apron, flame and chemical resistant coveralls, eyewash capable of sustained flushing, safety drench shower and hygienic facilities for washing.

---------------------------------------------------------------------------------------------------------------------------

The information herein is believed to be accurate and reliable as of the date compiled.  However, Chemat Technology, Inc. makes no representation, warranty or guarantee of any kind with respect to the information on this data sheet or any use of the product based upon this information.

DATE PREPARED: June 1999