MATERIAL SAFETY DATA SHEET

CHEMAT TECHNOLOGY, INC.

9036 Winnetka Avenue

Northridge, CA 91324

(818) 727-9786, (818) 727-9477 FAX

-----------------------------------------------IDENTIFICATION-----------------------------------------------

CHEMICAL NAME: Magnesium 2-methoxyethoxide, in 2-methoxyethanol

CATALOG NUMBER: M106

FORMULA: Mg(OCH2CH2OCH3)2		FORMULA WEIGHT: 174.38

TSCA: not listed in TSCA inventory	2-Methoxyethanol: listed

CHEMICAL FAMILY: Metal alkoxide solution

-------------------------------------HAZARDOUS INGREDIENTS---------------------------------------

HAZARDOUS INGREDIENTS:	%

Title compound	5	ACGIH(TLV): No data

OSHA/PEL: No data

2-Methoxyethanol	95 	ACGIH(TLV): 5ppm

OSHA/PEL: 25ppm

------------------------------------------------PHYSICAL DATA-----------------------------------------------

APPEARANCE AND ODOR: Clear yellowish liquid

MELTING POINT: -85oC (2-methoxyethanol) 	BOILING POINT: 124-125oC (2-methoxyethanol)

VAPOR PRESSURE: 6.2mm/20oC  		SPECIFIC GRAVITY: 0.965 (2-methoxyethanol)

(2-methoxyethanol)

SOLUBILITY IN WATER: Hydrolyzes in water

--------------------------------------------------FIRE HAZARD-------------------------------------------------

FLASH POINT: 115F or 46oC (2-methoxyethanol)

AUTOIGNITION TEMPERATURE: 545F or 284oC (2-methoxyethanol)

EXTINGUISHING MEDIA: Water spray.  Carbon dioxide, dry chemical powder or appropriate foam.

SPECIAL FIRE FIGHTING PROCEDURES: Wear self-contained breathing apparatus and protective clothing  to prevent contact with skin and eyes.  Combustible liquid.

UNUSUAL FIRE OR EXPLOSION HAZARDS: Forms exploxive mixtures in air.

-----------------------------------------------HEALTH HAZARD----------------------------------------------

MODE OF ENTRY:

INHALATION: Yes

SKIN CONTACT: Yes

EYE CONTACT: Yes

INGESTION: Yes

CARCINOGENCITY:

NTP: Not known

IARC: Not known

OSHA: Not known

EFFECTS OF OVEREXPOSURE:

INHALATION: Harmful by inhalation.  Irritating to respiratory system.

SKIN CONTACT: Irritating and readily absorbed to skin

EYE CONTACT: Irritating to eyes.

INGESTION: 2-methoxyethanol  is very toxic, may cause harm to the unborn child with possible risk of impaired fertility.  Soluble magnesium compounds may cause severe gastroenteritis, including abdominal pain, vomiting, and diarrhea.  May cause tremors, faintness, paralysis of the arms and legs, and slow or irregular heartbeat.  Severe cases may produce collapse and death due to respiratory failure.

EMERGENCY AND FIRST AID PROCEDURES:

INHALATION: Remove the victim to fresh air and seek medical attention if coughing, shortness of breath or irritation persists.

SKIN CONTACT: Wash the affected area with soap and water for at least 5 minutes.

EYE CONTACT: Immediately flush eyes, including under eyelids, with large amounts of water for at least 15 minutes.  Call a physician.

INGESTION: Give the victim plenty of water and seek immediate medical attention.

-----------------------------------------------REACTIVITY DATA--------------------------------------------

STABILITY: Moisture-sensitive material.

CONDITIONS TO AVOID: Contact with ignition source or heat.

INCOMPATIBILITY: Acid chlorides, acid anhydrides, oxidizing agents.

HAZARDOUS DECOMPOSITION PRODUCTS: Toxic fumes of carbon monoxide, carbon dioxide, magnesium oxide.

HAZARDOUS POLYMERIZATION: None

---------------------------------ENVIRONMENTAL INFORMATION--------------------------------

SPILL OR LEAKAGE PROCEDURES: Wearing full protective equipment, eliminate all sources of ignition.  Cover spill with dry sand or vermiculite.  Sweep up the mixture and dispose of properly.

WASTE DISPOSAL: Consult state, local, or federal EPA regulations for proper disposal.

----------------------------------PROTECTION AND PRECAUTIONS--------------------------------

VENTILATION REQUIREMENTS: Glove bag or box with dry, inert atmosphere.

RESPIRATORY PROTECTION: NIOSH/MSHA approved respirator with an organic vapor cartridge.

PROTECTIVE GLOVES: Rubber

EYE/FACE PROTECTION: ANSI approved safety goggles

HANDLING AND STORAGE: Handle and store the material under an inert atmosphere of nitrogen or argon.  Keep away from heat.

OTHER PRECAUTIONS: The material will react with air and moisture.  Lab coat and apron, flame and chemical resistant coveralls, eyewash capable of sustained flushing, safety drench shower and hygienic facilities for washing.

---------------------------------------------------------------------------------------------------------------------------

The information herein is believed to be accurate and reliable as of the date compiled.  However, Chemat Technology, Inc. makes no representation, warranty or guarantee of any kind with respect to the information on this data sheet or any use of the product based upon this information.

DATE PREPARED: August, 2009