MATERIAL SAFETY DATA SHEET

CHEMAT TECHNOLOGY INC.

9036 Winnetka Ave.

Northridge, CA  91324

(818) 727-9786, (818) 727-9477 FAX

-----------------------------------------------IDENTIFICATION-----------------------------------------------

CHEMICAL NAME: Molybdenum (V) ethoxide

CATALOG NUMBER: M407

FORMULA: Mo(OC2H5)5	FORMULA WEIGHT: 321.25

TSCA: not listed in TSCA inventory

CHEMICAL FAMILY: Metal alkoxide

-------------------------------------HAZARDOUS INGREDIENTS---------------------------------------

HAZARDOUS INGREDIENTS:	%

Title compound	  100	ACGIH(TLV): No data

OSHA/PEL: No data

------------------------------------------------PHYSICAL DATA-----------------------------------------------

APPEARANCE AND ODOR: Dark Green solid

MELTING POINT: No data	BOILING POINT: n/a

VAPOR PRESSURE: No data	SPECIFIC GRAVITY: No data

SOLUBILITY IN WATER: Reacts with water

--------------------------------------------------FIRE HAZARD-------------------------------------------------

AUTOIGNITION TEMPERATURE: No data

EXTINGUISHING MEDIA: Flammable.  Use alcohol foam, carbon dioxide or dry chemical extinguishing agents.

SPECIAL FIRE FIGHTING PROCEDURES: flammable.  Material readily ignited with flame, sparks, friction or heat.  Burning material may release toxic and corrosive fumes. Use normal fire fighting procedures which include wearing NIOSH/MSHA approved self-contained breathing apparatus, flame, and chemical resistant clothing; hats, boots, and gloves.  Leave the area unless fitted with a self-contained breathing apparatus and fire protective clothing.

-----------------------------------------------HEALTH HAZARD----------------------------------------------

MODE OF ENTRY:

INHALATION: Yes

SKIN CONTACT: Yes

EYE CONTACT: Yes

INGESTION: Yes

CARCINOGENCITY:

NTP: Not known

IARC: Not known

OSHA: Not known

EFFECTS OF OVEREXPOSURE:

INHALATION: May cause irritation of the nose and throat.  Exposure to high concentrations has a narcotic effect, producing symptoms of drowsiness, headache, staggering, unconciousness, and possibly death.

SKIN CONTACT: May cause irritation with stinging and burning sensations.  Causes defatting of the skin.

EYE CONTACT: Vapors may irritate the eyes.  Splashes may cause severe irritation, possible corneal burns and eye damage.

INGESTION: Molybdenum and its compounds are somewhat toxic.  Isopropyl alcohol may cause drowsiness, unconsciousness and death.  Gastrointestinal pain, cramps, nausea, vomiting, and diarrhea may also result.  The single lethal dose of isopropanol for a human adult is about 250 ml.

EMERGENCY AND FIRST AID PROCEDURES:

INHALATION: Remove the victim to fresh air and seek medical attention if coughing, shortness of breath or irritation persists.

SKIN CONTACT: Wash the affected area with soap and water for at least 5 minutes.

EYE CONTACT: Immediately flush eyes, including under eyelids, with large amounts of water for at least 15 minutes.  Call a physician.

INGESTION: Give the victim plenty of water and seek immediate medical attention.

-----------------------------------------------REACTIVITY DATA--------------------------------------------

STABILITY: Moisture-sensitive material.

CONDITIONS TO AVOID: Contact with ignition source or heat.

INCOMPATIBILITY: Moisture, heat, strong oxidizers, acetaldehyde, chlorine, ethylene oxide, hydrogen-palladium combination, nitroform, phosgene, hydrogen peroxide-sulfuric acid combination, potssium tert-butoxide, hypochlorous acid, isocyanates, oleum, perchloric acid, aluminum isopropoxide, crotonaldehyde.

HAZARDOUS DECOMPOSITION PRODUCTS: CO, CO2 MoO3, MoO2, and organic fumes

HAZARDOUS POLYMERIZATION: None

---------------------------------ENVIRONMENTAL INFORMATION--------------------------------

SPILL OR LEAKAGE PROCEDURES: Wearing full protective equipment, eliminate all sources of ignition.  Cover spill with dry sand or vermiculite.  Sweep up the mixture and dispose of properly.

WASTE DISPOSAL: Consult state, local, or federal EPA regulations for proper disposal.

----------------------------------PROTECTION AND PRECAUTIONS--------------------------------

VENTILATION REQUIREMENTS: Glove bag or box with dry, inert atmosphere.

RESPIRATORY PROTECTION: NIOSH/MSHA approved respirator with an organic vapor cartridge.

PROTECTIVE GLOVES: Rubber

EYE/FACE PROTECTION: ANSI approved safety goggles

HANDLING AND STORAGE: Handle and store the material under an inert atmosphere of nitrogen or argon.  Keep away from heat.

OTHER PRECAUTIONS: The material will react with air and moisture.  Lab coat and apron, flame and chemical resistant coveralls, eyewash capable of sustained flushing, safety drench shower and hygienic facilities for washing.

---------------------------------------------------------------------------------------------------------------------------

The information herein is believed to be accurate and reliable as of the date compiled.  However, Chemat Technology Inc. makes no representation, warranty or guarantee of any kind with respect to the information on this data sheet or any use of the product based upon this information.

DATE PREPARED:  April 21, 2005