MATERIAL SAFETY DATA SHEET

CHEMAT TECHNOLOGY, INC.

9036 Winnetka Avenue

Northridge, CA 91324

(818) 727-9786, (818) 727-9477 FAX

-----------------------------------------------IDENTIFICATION-----------------------------------------------

CHEMICAL NAME: Triethyl phosphite

CATALOG NUMBER: P103	PURITY: 98%

FORMULA: P(OCH2CH3)3	FORMULA WEIGHT: 166.16

TSCA: not listed in TSCA inventory	CAS#:	122-52-1

CHEMICAL FAMILY: Organophosphite

-------------------------------------HAZARDOUS INGREDIENTS---------------------------------------

HAZARDOUS INGREDIENTS:	%

Triethyl phospite	100

IRRITATION DATA

SKN-RBT 500 MG MLD                            ATDAEI 1,218,1992

EYE-RBT 100 MG MOD                            ATDAEI 1,218,1992

SKN-MAM 500 MG MLD                            MEPAAX 29,393,1978

EYE-MAM 100 MG MLD                            MEPAAX 29,393,1978

TOXICITY DATA

ORL-RAT LD50:1840 MG/KG                       ATDAEI 1,218,1992

IHL-RAT LC50:11063 MG/M3/6H                   ATDAEI 1,218,1992

ORL-MUS LD50:3720 MG/KG                       ATDAEI 1,218,1992

IHL-MUS LC50:6203 MG/M3/6H                    ATDAEI 1,218,1992

SKN-RBT LD50:2800 MG/KG                       ATDAEI 1,218,1992

------------------------------------------------PHYSICAL DATA-----------------------------------------------

APPEARANCE AND ODOR: Colorless liquid

MELTING POINT: No data		BOILING POINT: 156oC

DENSITY: 0.969 g/ml

SOLUBILITY IN WATER: air and moisture sensitive

--------------------------------------------------FIRE HAZARD-------------------------------------------------

FLASH POINT: 54oC

AUTOIGNITION TEMPERATURE: No data

EXTINGUISHING MEDIA: Use carbon dioxide, dry chemical extinguishing agents, and/or water fog.

SPECIAL FIRE FIGHTING PROCEDURES: Firefighters must use recommended protective equipment and self-contained breathing apparatus.

UNUSUAL FIRE OR EXPLOSION HAZARDS: Flammable liquid.  vapor accumulation could flash and/or explode if ignited.   When heated to decomposition, highly toxic fumes of POx may emits and react wigoriuslu with oxidizing materials.

-----------------------------------------------HEALTH HAZARD----------------------------------------------

MODE OF ENTRY:

INHALATION: Yes

SKIN CONTACT: Yes

EYE CONTACT: Yes

INGESTION: Yes

CARCINOGENCITY:

NTP: No

IARC: No

OSHA: No

EFFECTS OF OVEREXPOSURE:

Possibibly breathing problems if sufficient amounts are absorbed.  Asthma may be aggravated.  Possible mutagen.  Developmental abnormalities in the fetus have been reported.  Target organs are nerves, liver, kidneys, eyes, lung, bladder and reproductive organs.  May cause liver, lung, and reproductive damage based on animal data.  Absorption through the skin may lead to liver and pulmonary congestion.  Cataract formation and developmental abnormalities may occur.  Women of child-bearing potential should avoid exposure to the substance.

EMERGENCY AND FIRST AID PROCEDURES:

SKIN CONTACT: Wash contacted areas with soapand water.  If irritation develops, seek medical assitance.  Remove contaminated clothing and lauder before reuse.

EYE CONTACT: Flush with water for at least 15 minutes.  If irritation develops, seek medical assistance.

INGESTION: Do not induce vomiting.  Administer vegatable oil.  Get medical assistance. Note: Material if aspirated into the lungs may cause chemical pneumonitis.  Treat appropriately.

INHALATION: Remove from further exposure.  If unconsciousness occurs, seek immediate medical assistance and call a physician.  If breathing has stopped, use mouth to mouth resuscitation.

-----------------------------------------------REACTIVITY DATA--------------------------------------------

STABILITY: Stable.

CONDITIONS TO AVOID: Not established

INCOMPATIBILITY: Strong oxidizers and water.

HAZARDOUS DECOMPOSITION PRODUCTS: CO, CO2  phosphorous oxides, and/ or phosphine

HAZARDOUS POLYMERIZATION: None

---------------------------------ENVIRONMENTAL INFORMATION--------------------------------

SPILL OR LEAKAGE PROCEDURES: Eliminate all ignition sources.  Remove leaking containers to detached area.  Adsorb on fire retardent treated sawdust, diatomaceous earth, etc.  Shovel up and dispose of at an appropriate waste disposal facility in accordance with current applicable laws and regulations, and product characteristics at time of disposal. This combustible material may be burned in a chemical incinerator equipped with an afterburner and scrubber.  Observe all federal, state and local environmental regulations.

WASTE DISPOSAL: Dispose of waste by supervised incineration in compliance with applicable laws and regulations.  Rinse drums with acidified water, followed by water, prior to disposal or reuse.

----------------------------------PROTECTION AND PRECAUTIONS--------------------------------

VENTILATION REQUIREMENTS: Ventillation required and equipment must be explosion proof.  Use away from all ignition sources.

RESPIRATORY PROTECTION: Approved respiratory protective equipment must be used when vapor or mist concentrations exceed applicable standards.

PROTECTIVE GLOVES: Rubber or latex

EYE/FACE PROTECTION: ANSI approved safety goggles

HANDLING AND STORAGE: Keep away from heat.  Use in well ventilated area awat from all ignition sources.  Transport and use under a nitrogen blanket.

OTHER PRECAUTIONS:  Lab coat and apron, flame and chemical resistant coveralls, eyewash capable of sustained flushing, and hygienic facilities for washing.

---------------------------------------------------------------------------------------------------------------------------

The information herein is believed to be accurate and reliable as of the date compiled.  However, Chemat Technology, Inc. makes no representation, warranty or guarantee of any kind with respect to the information on this data sheet or any use of the product based upon this information.

DATE PREPARED: Sept. 27, 1999