## MATERIAL SAFETY DATA SHEET

CHEMAT TECHNOLOGY, INC.

9036 Winnetka Avenue

Northridge, CA 91324

(818) 727-9786, (818) 727-9477 FAX

-----------------------------------------------IDENTIFICATION-----------------------------------------------

CHEMICAL NAME: Triisopropyl phosphite

CATALOG NUMBER: P107

FORMULA: P[OCH(CH3)2]3 , or C9H21O3P	FORMULA WEIGHT: 208.24

Assay: 95%

SYNONYMS: Organophosphite

CAS #: 116-17-6

Miscellaneous: This chemical is in the EPA inventory under TSCA.

Label Precautions Moisture-sensitive
Toxic
Irritant
Combustible liquid

-------------------------------------HAZARDOUS INGREDIENTS---------------------------------------

HAZARDOUS INGREDIENTS:	%

Title compound				95		ACGIH(TLV): No data

OSHA/PEL: No data

ORL-RAT LD50:167 MG/KG                       		ALBRW* #OPB-3,1984

SKN-RBT LD50:>2 GM/KG                         		ALBRW* #OPB-3,1984

------------------------------------------------PHYSICAL DATA-----------------------------------------------

APPEARANCE AND ODOR: colorless liquid.

FREEZING/MELTING POINT: -59oC	BOILING POINT: (°C) 63 to 64 / 11MM

VAPOR PRESSURE: <2MM 20 C 	SPECIFIC GRAVITY (H2O=1): 0.844

REFRACTIVE INDEX: 1.4110

SOLUBILITY IN WATER: react with water

--------------------------------------------------FIRE HAZARD-------------------------------------------------

COMBUSTIBLE LIQUID

FLASH POINT: 154°F, 67C
AUTOIGNITION TEMPERATURE: No data

EXTINGUISHING MEDIA:   water spray.  carbon dioxide, dry chemical powder or appropriate foam.

SPECIAL FIREFIGHTING PROCEDURES: Wear self-contained breathing apparatus and protective clothing to prevent contact with skin and eyes.

UNUSUAL FIRE AND EXPLOSIONS HAZARDS: emits toxic fumes under fire conditions.

-----------------------------------------------HEALTH HAZARD----------------------------------------------

Toxic

MODE OF ENTRY:

INHALATION: Yes

SKIN CONTACT: Yes

EYE CONTACT: Yes

INGESTION: Yes

CARCINOGENCITY:

NTP: No data

IARC: No data

OSHA: No data

Target Organs: None

Potential Health Effects: The toxicological properties of this material have not been investigated.  Use appropriate procedures to prevent opportunities for direct contact with the skin or eyes and to prevent inhalation

----------------------------------------------- FIRST-AIDS------------------------------------------

EYE CONTACT: In case of contact, immediately flush eyes with copious amounts of  water for at least 15 minutes.

SKIN CONTACT: in case of contact, immediately wash skin with soap and copious amounts of water.

INHALATION: if inhaled, remove to fresh air. If not breathing give artificial

respiration. If breathing is difficult, give oxygen.

INGESTION: if swallowed, wash out mouth with water provided person is conscious call a physician.

wash contaminated clothing before reuse.

-----------------------------------------------REACTIVITY DATA--------------------------------------------

STABILITY: miosture sensitive

CONDITIONS TO AVOID: keep away from heat and open flame.

INCOMPATIBILITIES: Bases.  Oxidizing agents.

HAZARDOUS DECOMPOSITION PRODUCTS:  Carbon monoxide, carbon dioxide,  irritating and toxic fumes and gases. Thermal decomposition may produce toxic fumes of phosphorus oxides and/or phosphine.

HAZARDOUS POLYMERIZATION:  Has not been reported.

---------------------------------ENVIRONMENTAL INFORMATION--------------------------------

SPILL OR LEAKAGE PROCEDURES: Wear self-contained breathing apparatus, rubber boots and heavy rubber gloves. Cover with dry lime or soda ash, pick up, keep in a closed container and hold for waste disposal. Ventilate area and wash spill site after material pickup is complete.

WASTE DISPOSAL: This combustible material may be burned in a chemical incinerator equipped with an afterburner and scrubber. Observe all federal, state and local environmental regulations.

---------------------------------PROTECTION INFORMATION-------------------------------------------

RESPIRATORY PROTECTION: NIOSH/MSHA approved dust mask for ordinary use, self-contained breathing apparatus for emergency use.

PROTECTIVE GLOVES: Rubber

EYE/FACE PROTECTION: ANSI approved safety goggles

-----------------------------------SPECIAL PRECAUTIONS-----------------------------------------------------

chemical safety goggles. rubber gloves. niosh/msha-approved respirator. safety shower and eye bath. use only in a chemical fume hood. do not breathe vapor. do not get in eyes, on skin, on clothing. wash thoroughly after handling.

toxic. irritant.     keep tightly closed.     moisture sensitive    keep away from heat and open flame.    store in a cool dry place.

---------------------------------------------------------------------------------------------------------------------------

The information herein is believed to be accurate and reliable as of the date compiled.  However, Chemat Technology, Inc. makes no representation, warranty or guarantee of any kind with respect to the information on this data sheet or any use of the product based upon this information.

DATE PREPARED: July 28, 1999