MATERIAL SAFETY DATA SHEET

CHEMAT TECHNOLOGY INC.

9036 Winnetka Avenue

Northridge, CA 91324

(818) 727-9786, (818) 727-9477 FAX

-----------------------------------------------IDENTIFICATION-----------------------------------------------

CHEMICAL NAME: Sodium n-butoxide

CATALOG NUMBER: S507

FORMULA: (NaOC4H9n)	FORMULA WEIGHT: 96.11

CAS#: 2372-45-4

-------------------------------------HAZARDOUS INGREDIENTS---------------------------------------

HAZARDOUS INGREDIENTS:	%

Title compound	20	ACGIH(TLV): 0.5mg Na/m3-soluble compounds

n-butanol	80	OSHA/PEL: No data

Components subject to reporting requirements of Section 313 of the Emergency Planning and Community Right-to-Know Act:

Title compound: listed

------------------------------------------------PHYSICAL DATA-----------------------------------------------

APPEARANCE AND ODOR: colorless liquid

MELTING POINT: -210C	BOILING POINT: N/A

VAPOR PRESSURE: No data	SPECIFIC GRAVITY: 0.861

SOLUBILITY IN WATER: Reacts with water

--------------------------------------------------FIRE HAZARD-------------------------------------------------

FLASH POINT: No data

AUTOIGNITION TEMPERATURE: No data

EXTINGUISHING MEDIA: Dry chemical extinguisher, dry soda ash, or dry sodium chloride.  Do not use water or carbon dioxide.

SPECIAL FIRE FIGHTING PROCEDURES: Protect against caustic dust, smoke and water.  Wear pressure demand self-contained breathing apparatus with full facepiece and full protective clothing.

UNUSUAL FIRE OR EXPLOSION HAZARDS: Irritating fumes and caustic vapors may develop when material is exposed to elevated temperatures or open flames.

-----------------------------------------------HEALTH HAZARD----------------------------------------------

MODE OF ENTRY:

INHALATION: Yes

SKIN CONTACT: Yes

EYE CONTACT: Yes

INGESTION: Yes

CARCINOGENCITY:

NTP: Not known

IARC: Not known

OSHA: Not known

EFFECTS OF OVEREXPOSURE:

INHALATION: Will cause sneezing, irritation and burns.

SKIN CONTACT: Will cause irritation and burns.  If skin and air are dry, powder on skin may not cause irritation or burns.  Worker will notice a slippery feeling when washing.  However, if moisture is present, the powder can cause severe burns.

EYE CONTACT: Sodium t-butoxide will cause immediate or delayed severe caustic burns to the eyes.

INGESTION: Avoid ingestion of powder.

EMERGENCY AND FIRST AID PROCEDURES:

INHALATION: Remove the victim to fresh air and seek immediate medical attention if coughing, shortness of breath or irritation persists.

SKIN CONTACT: Wash the affected area with soap and water for at least 15 minutes.  Remove any contaminated clothing.

EYE CONTACT: Immediately flush eyes, including under eyelids, with large amounts of water for at least 15 minutes.  Seek medical attention.

INGESTION: Seek immediate medical attention.

-----------------------------------------------REACTIVITY DATA--------------------------------------------

STABILITY: Stable under nitrogen or argon in sealed containers.

CONDITIONS TO AVOID: Material decomposes slowly in contact with moist air and rapidly in contact with water, possibly igniting.  Avoid contact with moist air, water, acids, alcohols, ketones, esters, carbon dioxide, halogens.

HAZARDOUS DECOMPOSITION PRODUCTS: Sodium hydroxide, t-butanol and caustic organic vapors.

HAZARDOUS POLYMERIZATION: Not known.

---------------------------------ENVIRONMENTAL INFORMATION--------------------------------

SPILL OR LEAKAGE PROCEDURES: Wearing full protective equipment, eliminate all sources of ignition.  Cover spill with dry sand or vermiculite.  Sweep up the mixture and dispose of properly.

WASTE DISPOSAL: Consult state, local, or federal EPA regulations for proper disposal.

----------------------------------PROTECTION AND PRECAUTIONS--------------------------------

VENTILATION REQUIREMENTS: Glove bag or box with dry, inert atmosphere.

RESPIRATORY PROTECTION: NIOSH/MSHA approved respirator with an organic vapor cartridge.

PROTECTIVE GLOVES: Rubber

EYE/FACE PROTECTION: ANSI approved safety goggles

HANDLING AND STORAGE: Handle and store the material under an inert atmosphere of nitrogen or argon.  Keep away from heat.

OTHER PRECAUTIONS: The material will react with air and moisture.  Lab coat and apron, flame and chemical resistant coveralls, eyewash capable of sustained flushing, safety drench shower and hygienic facilities for washing.

---------------------------------------------------------------------------------------------------------------------------

The information herein is believed to be accurate and reliable as of the date compiled.  However, Chemat Technology, Inc. makes no representation, warranty or guarantee of any kind with respect to the information on this data sheet or any use of the product based upon this information.

DATE PREPARED: Mar. 2010.