MATERIAL SAFETY DATA SHEET

CHEMAT TECHNOLOGY INC.

9036 Winnetka Ave.

Northridge, CA  91324

(818) 727-9786, (818) 727-9477 FAX

-----------------------------------------------IDENTIFICATION-------------------------------------

CHEMICAL NAME: Tellurium isopropoxide

CATALOG NUMBER: T202	PURITY: 99.9%

FORMULA: Te(OC3H7i)4	FORMULA WEIGHT: 363.73

TSCA: not listed in the TSCA inventory

CHEMICAL FAMILY: Metal alkoxide

-------------------------------------HAZARDOUS INGREDIENTS-------------------------------

HAZARDOUS INGREDIENTS:	%

Title compound	100 	ACGIH(TLV): 0.1mgTe/m3

OSHA/PEL: 0.1mgTe/m3

------------------------------------------------PHYSICAL DATA--------------------------------------

APPEARANCE AND ODOR: Dark clear liquid

MELTING POINT: No data	BOILING POINT: 76oC/0.5mm

VAPOR PRESSURE: No data	SPECIFIC GRAVITY: No data

SOLUBILITY IN WATER: Decomposes in water

--------------------------------------------------FIRE HAZARD----------------------------------------

FLASH POINT: No data

AUTOIGNITION TEMPERATURE: No data

EXTINGUISHING MEDIA: Flammable liquid.  Use alcohol foam, carbon dioxide or dry chemical extinguishing agents.  Water may be used to keep fire exposed containers cool.

SPECIAL FIRE FIGHTING PROCEDURES: Flammable liquid.  Burning material may release toxic and corrosive fumes.  Use normal fire fighting procedures which include wearing NIOSH/MSHA approved self-contained breathing apparatus, flame, and chemical resistant clothing; hats, boots, and gloves.  Leave the area unless fitted with a self-contained breathing apparatus and fire protective clothing.

UNUSUAL FIRE OR EXPLOSION HAZARDS: No unusual fire or explosion hazards.

-----------------------------------------------HEALTH HAZARD-------------------------------------

MODE OF ENTRY:

INHALATION: Yes

SKIN CONTACT: Yes

EYE CONTACT: Yes

INGESTION: Yes

CARCINOGENCITY:

NTP: Not known

IARC: Not known

OSHA: Not known

EFFECTS OF OVEREXPOSURE:

Tellurium oxide: Subcutaneous (rat): TDLo; 798mg/kg (effects on embryo, specific developmental abnormalities - central nervous system, eyes and ears).  Intratracheal (rat): LDLo; 120mg/kg.

EMERGENCY AND FIRST AID PROCEDURES:

INHALATION: Remove the victim to fresh air and seek medical attention if coughing, shortness of breath or irritation persists.

SKIN CONTACT: Wash the affected area with soap and water for at least 5 minutes.

EYE CONTACT: Immediately flush eyes, including under eyelids, with large amounts of water for at least 15 minutes.  Call a physician.

INGESTION: Give the victim plenty of water and seek immediate medical attention.

-----------------------------------------------REACTIVITY DATA-----------------------------------

STABILITY: Moisture-sensitive material.

CONDITIONS TO AVOID: Contact with ignition source or heat.

INCOMPATIBILITY: Moisture, heat, strong oxidizers

HAZARDOUS DECOMPOSITION PRODUCTS: CO, CO2, tellerium oxide, and organic fumes

HAZARDOUS POLYMERIZATION: None

---------------------------------ENVIRONMENTAL INFORMATION-------------------------

SPILL OR LEAKAGE PROCEDURES: Wearing full protective equipment, eliminate all sources of ignition.  Cover spill with dry sand or vermiculite.  Sweep up the mixture and dispose of properly.

WASTE DISPOSAL: Consult state, local, or federal EPA regulations for proper disposal.

----------------------------------PROTECTION AND PRECAUTIONS------------------------

VENTILATION REQUIREMENTS: Glove bag or box with dry, inert atmosphere.

RESPIRATORY PROTECTION: NIOSH/MSHA approved respirator with an organic vapor cartridge.

PROTECTIVE GLOVES: Latex or rubber.

EYE/FACE PROTECTION: ANSI approved safety goggles

HANDLING AND STORAGE: Handle and store the material under an inert atmosphere of nitrogen or argon.  Keep away from heat.

OTHER PRECAUTIONS: The material will react with air and moisture.  Lab coat and apron, flame and chemical resistant coveralls, eyewash capable of sustained flushing, safety drench shower and hygienic facilities for washing.

----------------------------------------------------------------------------------------------------------------

The information herein is believed to be accurate and reliable as of the date compiled.  However, Chemat Technology, Inc. makes no representation, warranty or guarantee of any kind with respect to the information on this data sheet or any use of the product based upon this information.

DATE PREPARED:  December 23, 2005