MATERIAL SAFETY DATA SHEET

CHEMAT TECHNOLOGY, INC.

9036 Winnetka Avenue

Northridge, CA 91324

(818) 727-9786, (818) 727-9477 FAX

-----------------------------------------------IDENTIFICATION-----------------------------------------------

CHEMICAL NAME: Thallium Ethoxide

CATALOG NUMBER: T402

FORMULA: Tl(OC2H5)	FORMULA WEIGHT: 249.43

CAS #:  20398-06-5

----------------------------------------HAZARDOUS INGREDIENTS------------------------------------

# HAZARDOUS INGREDIENTS:	%

Title compound	100	ACGIH(TLV): No data

OSHA/PEL: No data

------------------------------------------------PHYSICAL DATA-----------------------------------------------

APPEARANCE:  Cloudy, dense liquid

MELTING POINT: -3 oC 			BOILING POINT:  130 oC

VAPOR PRESSURE: No data	SPECIFIC GRAVITY: 3.493

SOLUBILITY IN WATER: Reacts with water

--------------------------------------------------FIRE HAZARD-------------------------------------------------

FLASH POINT: >230 oF

AUTOIGNITION TEMPERATURE: No data

EXTINGUISHING MEDIA: CO2 or dry powder.

SPECIAL FIRE FIGHTING PROCEDURES: Combustible. If involved in a fire or heated to high temperatures the material may burn. Burning material mat release toxic and corrosive fumes. Leave area unless fitted with a self-contained breathing apparatus and fire protective clothing.

UNUSUAL FIRE AND EXPLOSION HAZARDS: None.

-----------------------------------------------HEALTH HAZARD----------------------------------------------

MODE OF ENTRY:

INHALATION: No

SKIN CONTACT: Yes

EYE CONTACT: Yes

INGESTION: Yes

CARCINOGENCITY:

NTP: No

IARC: No

OSHA: No

EFFECTS OF OVEREXPOSURE:

Acute thallium poisoning results in swelling of the feet and legs, vomiting, insomnia, mental confusion, severe pain in the legs and loin, angina-like pain, nephritis and weakness. Can be fatal.

EMERGENCY AND FIRST AID PROCEDURES:

INHALATION: Remove victim to fresh air and seek medical attention.

SKIN CONTACT: Flush skin with water, then wash with soap and water for at least 5 minutes.

EYE CONTACT: Flush with clean water for at least 15 minutes and consult physician then, 	get medical attention immediately.

INGESTION: Give the victim plenty of water and seek immediate medical attention.

-----------------------------------------------REACTIVITY DATA--------------------------------------------

STABILITY: Moisture-senstive material

CONDITIONS TO AVOID: None

INCOMPATIBILITY: Oxidizing agents

HAZARDOUS DECOMPOSITION: Ethanol and thallium oxide

HAZARDOUS POLYMERIZATION: None

---------------------------------ENVIRONMENTAL INFORMATION--------------------------------

SPILL OR LEAKAGE PROCEDURES: Small spills can be absorbed into vermiculite or other suitable absorbent. Sweep up the material and dispose of  properly.

WASTE DISPOSAL: Material should be disposed of in accordance with local, state and federal regulations.

----------------------------------PROTECTION AND PRECAUTIONS--------------------------------

VENTILATION REQUIREMENTS: efficient fume hood

RESPIRATORY PROTECTION: NIOSH/MSHA  approved dust mask

PROTECTIVE GLOVES: Rubber

EYE/FACE PROTECTION: goggles.

HANDLING AND STORAGE: Handle and store the material under an inert atmosphere of nitrogen or argon. Keep away from heat or moisture.

OTHER PRECAUTIONS: None

---------------------------------------------------------------------------------------------------------------------------

The information herein is believed to be accurate and reliable as of the date compiled.  However, Chemat Technology, Inc. makes no representation, warranty or guarantee of any kind with respect to the information on this data sheet or any use of the product based upon this information.

DATE PREPARED: October 1999