MATERIAL SAFETY DATA SHEET

CHEMAT TECHNOLOGY, Inc.

9036 Winnetka Avenue

Northridge, CA 91324

(818) 727-9786, (818) 727-9477 FAX

-----------------------------------------------IDENTIFICATION-------------------------------------

CHEMICAL NAME: Ytterbium bis (2,2,6,6-tetramethyl-3,5-heptanedionate)

CATALOG NUMBER: Y114 		PURITY: 99.9%

FORMULA: Yb(C11H19O2)3	FORMULA WEIGHT: 722.86

CAS #:  15492-52-1

-------------------------------------HAZARDOUS INGREDIENTS-------------------------------HAZARDOUS INGREDIENTS:	%

Title compound	100 	ACGIH(TLV): No data

OSHA/PEL: No data

Components subject to reporting requirements of Section 313 of the Emergency Planning and Community Right-to-Know Act:

Title compound: not listed

------------------------------------------------PHYSICAL DATA--------------------------------------

APPEARANCE: Off-white crystalline solid

MELTING POINT: 167oC	BOILING POINT:  No data

VAPOR PRESSURE: No data 	SPECIFIC GRAVITY: No data

SOLUBILITY IN WATER: Insoluble, immiscible.

--------------------------------------------------FIRE HAZARD----------------------------------------

FLASH POINT: No data

AUTOIGNITION TEMPERATURE: No data

EXTINGUISHING MEDIA: Use foam or dry powder.  Water spray may be used.  For small fires, CO2 is also suitable.

UNUSUAL FIRE OR EXPLOSION HAZARDS:  No special firefighting procedures needed, use normal procedures which include wearing NIOSH/MSHA approved self-contained breathing apparatus, flame and chemical resistant clothing; hats, boots and gloves.  If without risk, remove material from fire area.

-----------------------------------------------HEALTH HAZARD-------------------------------------MODE OF ENTRY:

INHALATION: Yes

SKIN CONTACT: Yes

EYE CONTACT: Yes

INGESTION: Yes

CARCINOGENCITY:

NTP: Not known

IARC: Not known

OSHA: Not known

EFFECTS OF OVEREXPOSURE:

INGESTION: Presumed to slowly decomposes to metabolisable organic residues

SKIN CONTACT:  Irritant if crosses dermal barrier, rendering skin susceptible to dermatitis.

EYE CONTACT:  Repeated contact may lead to opaque barrier on cornea.

INHALATION:  Harmful dust.

EMERGENCY AND FIRST AID PROCEDURES:

INHALATION: Remove the victim to fresh air and seek medical attention if coughing, shortness of breath or irritation persists.

SKIN CONTACT: Wash the affected area with ethanol first, then soap and water for at least 5 minutes.

EYE CONTACT: Immediately flush eyes, including under eyelids, with large amounts of water for at least 15 minutes.  Call a physician.

INGESTION: Give the victim plenty of water and seek immediate medical attention.

-----------------------------------------------REACTIVITY DATA-----------------------------------

STABILITY: Moisture-sensitive material.

CONDITIONS TO AVOID: Contact with ignition source or heat.

INCOMPATIBILITY: Moisture, sparks, open flames, oxidizers, water, acids.

HAZARDOUS DECOMPOSITION PRODUCTS: Thermal decomposition produces propylene, CO, CO2, and ytterbium oxide.

HAZARDOUS POLYMERIZATION: None

---------------------------------ENVIRONMENTAL INFORMATION-------------------------

SPILL OR LEAKAGE PROCEDURES: Wearing full protective equipment, eliminate all sources of ignition.  Cover spill with dry sand or vermiculite.  Sweep up the mixture and dispose of properly.

WASTE DISPOSAL: Consult state, local, or federal EPA regulations for proper disposal.

----------------------------------PROTECTION AND PRECAUTIONS------------------------

VENTILATION REQUIREMENTS: Glove bag or box with dry, inert atmosphere.

RESPIRATORY PROTECTION: NIOSH/MSHA approved respirator with an organic vapor cartridge.

PROTECTIVE GLOVES: Rubber

EYE/FACE PROTECTION: ANSI approved safety goggles

HANDLING AND STORAGE: Handle and store the material underan inert atmosphere of nitrogen or argon.  Keep away from heat.

OTHER PRECAUTIONS: The material will react with moisture.  Lab coat and apron, flame and chemical resistant coveralls, eyewash capable of sustained flushing, safety drench shower and hygienic facilities for washing.

----------------------------------------------------------------------------------------------------------------

The information herein is believed to be accurate and reliable as of the date compiled.  However, Chemat Technology, Inc. makes no representation, warranty or guarantee of any kind with respect to the information on this data sheet or any use of the product based upon this information.

DATE PREPARED: October, 1997